## Slide 1: IIoT Fundamentals and Applications Presented by SME Chapter 112

## Slide 2: Who Am I?
My name is Adam Cook.
Studied Mechanical Engineering at Purdue University West Lafayette.
Chief Technical Officer of Alliedstrand in Chicago (we also have engineers in Dallas).
Chair of SME Chapter 112 (Northwest Indiana and Chicagoland). Check out sme112.org.
I work with embedded systems, robotics, automation systems and industrial software.
Contact my chapter at hello@sme112.org.

## Slide 3: SME Virtual Network Slack
Are you an SME member? Do you want access to Slack? Fill out this short form: http://bit.ly/2BpjMiE

## Slide 4: Agenda
Part 1 - IIoT High-Level Tour and Engineering/Manufacturing Use Cases. Break
Part 2 – IIoT protocols, architectures, communications, IT/OT considerations and security.
Slides:
http://bit.ly/2HOb7GE

## Slide 5: What is IoT?
Internet of Things (IoT) is (loosely) a broad term referring to a network of devices (or “things”) which can interoperate with the Internet.
IoT is sometimes called Internet of Everything (IoE).
A Thing is a physical object that can communicate via a network.
Things are decoupled from software applications/services in IoT.
Slides:
http://bit.ly/2HOb7GE

## Slide 6: Sensors
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2G7VEny
Notes: Sensors sense and measure changes in the physical world.

## Slide 7: Actuators
Slides:
http://bit.ly/2HOb7GE
Motors
Cylinders
Servo Valve
Notes: Actuators do useful work on the physical world.

## Slide 8: IoT connects…
Things
Systems
Business Applications
ERP
PLM
CRM
Control Systems
People
Consumers
Decision Makers
Partners
Employees
Slides:
http://bit.ly/2HOb7GE

## Slide 9: Question
Slides:
http://bit.ly/2HOb7GE
Can you think of any commonly-used IoT devices?
Notes: Mobile phone!

## Slide 10: Connection Types
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2otKGih

## Slide 11: Coupled
Early 1990s Home Automation System
Relay
What is the ROI on this?
Slides:
http://bit.ly/2HOb7GE

## Slide 12: Decoupled
Source: http://dell.to/2u5mF6t
Cloud
Big Data
Machine Learning
Analytics
Probably an IoT Gateway here.
Device Network
Slides:
http://bit.ly/2HOb7GE

## Slide 13: Decoupled
Data Analytics
Data Analytics
Analyze data from devices.
Network Analytics
Analyze data from the network architecture used to connect devices.
Machine Learning System(s)
Service Layer
To Device Network
Training Data
Slides:
http://bit.ly/2HOb7GE
Notes: Data Analytics – analyze and extract value generated by devices and sensors.
Network Analytics – network packet metadata analysis (network problems, QoS), detection of cyber security attacks.

## Slide 14: Latency
Slides:
http://bit.ly/2HOb7GE
Cloud Computing Layer
Elastic compute, big data processing and data warehousing.
Fog Computing Layer IoT Gateway
Mist Computing Layer
Devices, sensors and actuators.
High Latency
Low Latency
Notes: Latency is a time interval between stimulation and response.

## Slide 15: So what’s with the “Internet” in IoT?
Slides:
http://bit.ly/2HOb7GE
Decoupled
Scalable (compute)
Global
Internet
Notes: Latency is a time interval between stimulation and response.

## Slide 16: IoT Challenges
Scale (Data and Network)
IoT has the possibility to scale to millions of devices.
Security/Privacy
Physical assets and IP can be at risk. This is a big one.
Interoperability
Devices and networks need to talk the same “language”.
Operational Issues IoT needs tight IT/OT coordination.
Implementation Commonality
IoT implements are largely made to order – particularly for the cloud services. Cost implications.
Slides:
http://bit.ly/2HOb7GE

## Slide 17: IT and OT
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2GKH6bk
Note this convergence.
Notes: IT – Information Technology – computers and supporting systems to store, retrieve, transmit and manipulate data.
IT is query based, non-real time and the data is largely at rest.
OT – Operational Technology – hardware (and hardware/software combination) used to detect and cause changes in physical processes.
OT is event based, real-time and the data is at motion.

## Slide 18: IT and OT Separation
Slides:
http://bit.ly/2HOb7GE
Purdue Model
Phishing
Spear phishing
USB/Physical equipment access
PLCs, HMIs
Notes: Differences in priorities between IT and OT.
IT – Focused on protecting a company’s digital assets.
OT – Focused on high OEE, safety, and “always on” operations.
IT – Emphasizes strict network access control (authentication and access policies).
OT – Emphasizes strict physical access control.
IT – Device failure is expected and fail-over and elasticity are designed in.
OT – Device failure causes concrete economic harm to a company.
IT – Upgrades and patches are applied ASAP.
OT – Only during scheduled downtime.

## Slide 19: Cyberattack Example Cases
December 2015 Ukraine power grid cyberattack
German steel mill cyberattack
Saudi Aramco and Qatar RasGas cyberattack (2012)
WannaCry ransomware attack
Slides:
http://bit.ly/2HOb7GE
Notes: Ukraine Power Grid Cyberattack – Spear-fishing
Saudi Aramco – business layer was at risk, but ICS layer was budgeted to be “secure”. Virus entered the business layer and infected security appliances and critical workstations.
WannaCry – exploited holes in old versions of the Windows operating system to infect systems. The UK’s National Health Service (NHS) was deeply effected.

## Slide 20: So what is IIoT?
IIoT stands for Industrial Internet of Things.
IIoT is sometimes called Industrial Internet.
IIoT is really a subcategory of IoT. Many of the technologies are the same (but not all) but it focuses on “industrial” use cases.
The business case for IIoT is increasing efficiency and safety while reducing costs.
Slides:
http://bit.ly/2HOb7GE
IoT
IIoT
Notes: Industrial use cases could include smart factories, transportation, logistics, building automation and smart cities.

## Slide 21: What is Industry 4.0?
Sometimes will hear that Industry 4.0 and IIoT are the same.
Technically, they are not.
Industry 4.0 (Industrie 4.0) is/was a German government program in digitizing manufacturing.
Industry 4.0 is also called the 4th Industrial Revolution.
Cyber Physical Systems, IIoT, advanced data analytics and machine learning.
Slides:
http://bit.ly/2HOb7GE

## Slide 22: IIoT Reference Models/Architectures
Purdue Enterprise Reference Architecture
Industrial Internet Reference Architecture (IIRA) by Industrial Internet Consortium (IIC).
Slides:
http://bit.ly/2HOb7GE
Notes: Purdue Model – segments devices and equipment into hierarchical functions.
IIRA – platform developed to drive interoperability, map applicable technologies and guide standards development.

## Slide 23: IIoT Reference Models/Architectures
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2zpBpeN
Notes: Purdue Model – segments devices and equipment into hierarchical functions.
IIRA – platform developed to drive interoperability, map applicable technologies and guide standards development.

## Slide 24: Use Case – Digital Twin
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2pqVZbo
3D Models
Physics-Based Models
Sensor Data
Data Analytics/Big Data
Machine Learning
Human Knowledge
Historical Data
Digital Simulations
Note: There is something like 20,000 sensors on a jet engine!
Notes: Rolls-Royce has a system for their engines as well.
Other popular examples of digital twins include Aircraft Engines, Wind Turbines, Offshore Rigs, Locomotives, Buildings and Whole Cities.

## Slide 25: Use Case – Smart City/Smart Building
Slides:
http://bit.ly/2HOb7GE
Smart phones, smart meters, networks of sensors and RFIDs.
Check out UI Labs’ City Tech iniatives.
LPWAN

## Slide 26: Use Case – Building Automation
Slides:
http://bit.ly/2HOb7GE
Can also be tied to larger “smart cities” effort.

## Slide 27: Use Case – Predictive Maintenance
Slides:
http://bit.ly/2HOb7GE
Using historical operational data to determine failure windows prior to them occurring.
Spindle bearing heat and vibration sensors
Heat sensors on ball screws
Machine bed vibration sensors
Coolant filter pressure sensors
What else can this data be used for?

## Slide 28: Use Case – (Smart) Factory Automation
Slides:
http://bit.ly/2HOb7GE
Cloud
Robot-to-robot.
Factory-to-cloud.
Factory-to-factory.
Finished product-to-factory.

## Slide 29: Use Case – Autonomous Vehicles
Slides:
http://bit.ly/2HOb7GE
Vehicle-to-vehicle.
Vehicle-to-cloud.
Vehicle-to-smart city.
Cloud
Source: http://intel.ly/2pr0xhX
CANbus
Notes: Network in most vehicles is a communication bus know as CANbus. This allows devices (usually internal to the vehicle) to communication with each other without a host computer.

## Slide 30: Use Case – Asset Tracking
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2HPC64z

## Slide 31: What about small/medium businesses?
Favor incremental steps to IIoT adoption over large projects.
IIoT is not magic. It is most useful when finding that “last mile” of efficiency.
Having the IT and OT personnel and expertise is critical.
Security needs to be budgeted in and enforced enterprise-wise. In a lot of ways, the attack surface is larger in IIoT.
Beware of legacy equipment challenges.
Careful! It can transform your enterprise (hopefully, for the better).
Slides:
http://bit.ly/2HOb7GE

## Slide 32: Break
Next up. We take a deeper technical dive into IoT/IIoT.
6LoWPAN: http://bit.ly/2GQSJ0E
Slides:
http://bit.ly/2HOb7GE

## Slide 33: IoT Stack Overview
Source: http://bit.ly/2G8zbHa
We will work up this way.
Slides:
http://bit.ly/2HOb7GE
Layers based on the OSI Model
Theoretically, you can pick and choose technologies from each layer independently from one another.
Layers based on the OSI Model
Notes: For example, you can “choose” UDP or TCP for the transport layer, but it is usually chosen for you by the application layer.
Some other models (besides the OSI Model), wrap up the “Session” layer into the “Application” layer.
OSI model is a little bit of a stretch for IoT.

## Slide 34: IoT Stack Overview + Some More Industrial
Source: http://bit.ly/2G8zbHa
Slides:
http://bit.ly/2HOb7GE
MTConnect
OPC-UA
Ethernet

## Slide 35: Physical and Datalink Layers
Contains embedded systems and sensors, but, more importantly, the standards which will connect to the Internet.
Slides:
http://bit.ly/2HOb7GE
Ethernet
WiFi (802.11b, g, n)
GSM, 3G, LTE, 4G, 5G
LPWAN

## Slide 36: Physical/Datalink Layers - LPWAN
Slides:
http://bit.ly/2HOb7GE
WLAN – Wireless Local Area Network (WiFi)
WWAN – Wireless Wide Area Network (Cellular)
LPWAN – Low-Power Wide Area Network
LPWANs are great for:
  Filling gaps between WLAN and WWAN.
  Devices that need great battery life.
  Transmission distance over 15 km.
  Capable of outdoor use.
  Low-cost.

## Slide 37: Other LPWAN Technologies
Slides:
http://bit.ly/2HOb7GE
aka LoRaWAN
aka LPWAN
aka WLAN
aka WWAN
Source: http://bit.ly/2IE7JPG

## Slide 38: Network Layer
Internet is here.
Provides a connection between networks and a connection between physical layers (to each other or to cloud services).
Unique identifier called an IP Address is here.
Slides:
http://bit.ly/2HOb7GE
IPv4
IPv6
RPL

## Slide 39: Network Layer – IPv4 vs. IPv6
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2IATz21
IPv6 Advantages:
Larger address space.
Better built-in security.
Harmonizes IoT datalink layer.

## Slide 40: Network Layer – IPv6
Slides:
http://bit.ly/2HOb7GE
IPv6 creates a common network layer for these technologies.

## Slide 41: Network Layer – IPv4 Address Exhaustion
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2GLxey5
IPv4 Exhaustion Point

## Slide 42: Transport Layer
TCP and UDP are here.
Data stream handling.
TCP – Transmission Control Protocol
UDP – User Datagram Protocol
UDP is popular for IoT use. TCP is popular for IIoT. These are not hard rules.
Slides:
http://bit.ly/2HOb7GE

## Slide 43: TCP vs. UDP
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2FNTfPz
Notes: TCP – suitable for applications that require high reliability, but transmission time and battery life is less critical. Examples include web browsing and e-mail.
UDP – suitable for applications that need fast and efficient transmission, but high reliability takes a back seat. Simpler protocol and therefore it is easier on the battery life. Examples include music streaming, games, VoIP.

## Slide 44: TCP vs. UDP
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2DHqwG4
Notes: TCP – suitable for applications that require high reliability, but transmission time and battery life is less critical. Examples include web browsing and e-mail.
UDP – suitable for applications that need fast and efficient transmission, but high reliability takes a back seat. Simpler protocol and therefore it is easier on the battery life. Examples include music streaming, games, VoIP.

## Slide 45: Application Layer
Contains value-added applications, communications protocols and interface methods for a network.
Does not really say anything about data formats used. It is common for large sensor networks to be involved in unstructured data transfer.
Slides:
http://bit.ly/2HOb7GE
MTConnect
MQTT
OPC-UA
HTTP

## Slide 46: Application Layer - HTTP
Slides:
http://bit.ly/2HOb7GE

## Slide 47: Application Layer - MQTT*
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2GLXCrG
Publisher
Subscribers
Notes: Means that this topic will be addressed in detail within its own webinar or part of a workshop.

## Slide 48: Application Layer – MQTT QoS
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2FW4iSO
Notes: Means that this topic will be addressed in detail within its own webinar or part of a workshop.
PUBLISH – Publish message.
PUBACK – Publish acknowledgement.
PUBREC – Publish received.
PUBREL – Publish release.
PUBCOMP – Publish complete.

## Slide 49: Web Stack vs. IoT Stack
Slides:
http://bit.ly/2HOb7GE
HTML
HTTP
TLS
TCP
IPv6
Messages
MQTT
TLS
TCP
6LoWPAN
Web
IoT

## Slide 50: MTConnect*
Slides:
http://bit.ly/2HOb7GE
Source: http://bit.ly/2G4QMjh
XML data format
Provides REST interface
Notes: Technical standard to retrieve process information from NC machine tools.

## Slide 51: OPC-UA*
Slides:
http://bit.ly/2HOb7GE
Image credit ascolab
Notes: Machine-to-machine communication protocol for industrial automation.
OPC-UA is the successor to OPC Classic.

## Slide 52: Other Automation Protocols*
Slides:
http://bit.ly/2HOb7GE
CANbus

## Slide 53: Upcoming Webinars
Slides:
http://bit.ly/2HOb7GE
We will dive down to the code level with these technologies:

## Slide 54: Thank you!
Want to learn more about
?
Check out sme.org
Questions? Ask in the Live Chat or Slack or check the feedback link in the description!
Slides:
http://bit.ly/2HOb7GE